## Slide 1: The benchmark is a network of six surrogate nodes in four priced stages each node is a Gaussian process whose output feeds its children
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
critical-mineral burden: known from the composition, costs nothing
Notes: Seven inputs: four composition levels (Zn+Mg, Cu, Zr, Sc), the atomizer setting, laser power and scan speed. CALPHAD returns three things for one composition in one $10 call: strengthening-phase fraction, freezing range and primary-nucleant fraction. Atomization returns powder quality from the atomizer setting and the nucleant fraction ($1,500 a run). The print returns a dense, crack-free fraction from power, speed, freezing range, nucleant fraction and powder quality ($2,500 a build). The tensile test returns strength from the strengthening phase and the density ($200 a bar). The objective is strength minus 0.3 times a critical-mineral burden that is known from the composition and costs nothing. Costs are the abstract's; the $10 for CALPHAD is an assumption.

## Slide 2: One Gaussian process per node; each child sees its parents' outputs an observation anywhere updates everything downstream
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
critical-mineral burden: known from the composition, costs nothing
Notes: This is the BOFN model (Astudillo and Frazier 2021): one GP per node, fitted on that node's own inputs, including the outputs of its parents. The bell on an edge is the forwarded posterior. A CALPHAD result therefore changes what the model believes about powder quality, printability and strength before anything is made.

## Slide 3: Simulate one composition for $10 one call returns all three CALPHAD outputs; nothing has to exist first
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
Notes: The cheapest move. pKGFN scores it like the others: knowledge gradient per dollar.

## Slide 4: Atomize one powder lot for $1,500 needs the alloy's CALPHAD result; the lot can be printed many times
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
Notes: The powder node takes the atomizer setting and the nucleant fraction, so the alloy must have been simulated (the benchmark runs CALPHAD automatically before a first melt). A lot, once made, can be printed again and again: that is where partial evaluation pays.

## Slide 5: Print one build for $2,500 from a powder that exists, with one power and speed
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
Notes: The most expensive node. It needs an existing lot; one build carries one laser power and scan speed.

## Slide 6: Test one bar for $200 from a build that exists
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
Notes: Strength is the only node that reaches the objective directly; a build sits untested until this is bought.

## Slide 7: Or run the whole chain for $4,210 what standard BO, random search, tiered screening and full-pipeline BOFN buy per design
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
Notes: Every other policy in the benchmark buys all four stages for each design it picks. pKGFN and the powder-reuse ablation are the only ones that can stop part-way.

## Slide 8: The effect a CALPHAD screen cannot see Zr and Sc nucleants suppress hot cracking in the print; the screen ranks alloys on strength and freezing range alone
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
critical-mineral burden: known from the composition, costs nothing
nucleant suppresses
hot cracking
Notes: The one simulation-versus-experiment gap built into the benchmark (kappa). Zr-inoculated 7075 and 6061 print crack-free although their freezing range says they should not (Martin et al., Nature 2017). Tiered screening keeps the four strongest alloys with a freezing-range index below 0.25 and never looks at this edge, so its shortlist misses the inoculated optimum. At kappa = 0 the edge does nothing and the screen is exactly right.

## Slide 9: pKGFN buys one node at a time, by knowledge gradient per dollar the full-pipeline policies buy the whole chain
Inputs
CALPHAD $10
Atomize $1,500
Print $2,500
Test $200
Objective
one call
Strengthening
phase fraction
Freezing
range
Nucleant
fraction
Powder
quality
Dense,
crack-free
fraction
Strength
Strength
− 0.3 × burden
Composition
Zn+Mg, Cu, Zr, Sc
Atomizer
setting
Laser power,
scan speed
critical-mineral burden: known from the composition, costs nothing
Notes: Whole again. The question the benchmark asks: does choosing which node to evaluate next beat buying the chain for every design? See the results figure.